## Slide 1: GCBASIC
18FXXQ24 CHIPFAMILY

## Slide 2: GCBASIC 18FxxQ24
December 2024 release
GCBASIC
New chip family
The PWM challenge

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 4: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ24 chip family
GCBASIC is a cross platform with common code translation

## Slide 5: The core compiler
GCBASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
ASM file
Absolute Machine Code
HEX file
8 bit PIC, AVR, AVR-DX and LGT
Reports:
TXT and HTML
GCBASIC Compiler
Chip Specific DAT file
Chip Specific Constraints

## Slide 6: Hardware
GCBASIC prototype board
  8, 14, 18, 28 and 40 pin devices
  LEDs
  Switches
  POTs
  Connections
    USB, GLCD, LCD
    Sensors
PICKit2 using PICKitPlus
External power supply
USART/TTL adapter

## Slide 7: Setup
http://www.gabotronics.com/development-boards/xmega-xminilab.htm

## Slide 8: PWM
 | PWM type | Characteristics | PPS required | Comment
1 | The simplest way | Port on and off | No | Any port**
2 | The pulseout() way | PulseOut() a port for a period | No | Any port**
3 | The PWMOut() way | PWMOUT() a number of pulses | No | Any port**
4 | CCP/PWM way | Fixed frequency, fixed duty using timer2* | Yes – CCP/PWMx module | Low code impact, two constants
5 | CCP/PWM way | Variable frequency, variable duty using timer2* | Yes – CCP/PWMx module | ASM does the heavy lifting
6 | PWM 16 bit way | Wide range of capabilities | Yes - PWMxx | Lots of parameters
7 | Timer interrupt way | Use a timer1* | No | Any port**
* could use other timers
** any valid output

## Slide 9: LAB
Try to get PWM to work!

## Slide 10: Summary findings
DAT memory specification section ( ‘[FreeRAM]’ ) was incorrect - resolved
  [FreeRAM] RAM location – fixed within GETCHIPDATA.BAS
  ADC initially shows no results
  Wrong connection on the test rig!
EEPROM demo program not working as expected
  EEPROM.H required updating
I2C does not operate as per datasheet
  HWI2C.H updated
PWM Registers & Register.Bits fundamentally different
  PWM.H required updating
PPSTOOL does not support Q24
  Edit XML to represent this new family
Issue Noted
  Compiler does not handle undefined port.bit appropriate portc.7

## Slide 11: GCBASIC 18FxxQ24
November 2024 release
GCBASIC
Like and subscribe!
New chip family – getting the basics operating