## Slide 1: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 4 – sequence the LEDs

## Slide 2: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 4 – sequence the LEDs
January 2025

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC16Fxxxx
PIC16Fxxxx is a high performance PIC16
  Digital and Analog peripherals
  8 –bit or 10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
The PIC16 offers 8, 14,18,20, 28, 40 and 48-pin packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, EEPROM and DATA blocks
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC supports the 16Fxxxx chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the PIC attached
  You have the 4 LEDs operating
  You have a POT connected

## Slide 8: Hardware
The PICDEM 2 Plus Demonstration Board
18-, 28- and 40-pin DIP sockets (although three sockets are provided, only one device may be used at a time)
On-board, +5V regulator for direct input from 9V, 100 mA AC/DC wall adapter or 9V battery, or hooks for a +5V, 100 mA regulated DC supply
RS-232 socket and associated hardware for direct connection to an RS-232 interface
Programmer/debugger connectivity supporting MPLAB® ICD 3, MPLAB REAL ICE, PICkit 2 and PICkit 3
PICkit Serial Connector for analysis of serial communications peripherals such as SPI or I2C™
5 k pot for devices with analog inputs
Three push button switches for external stimulus and Reset
Power-on indicator LED
Four LEDs connected to PORTB
On-board external oscillators including: a) Unpopulated DIP socket for canned crystal oscillator (Y2) b) RC oscillator circuit (R4, C3) c) Unpopulated holes for crystal connection (Y1) d) 32.768 kHz crystal for Timer1 clock operation (Y3)
32K x 8 Serial EEPROM
LCD display
Piezo buzzer
Prototype area for user hardware
Expansion Header for PICtail™ daughter card connectivity or user access to
MCUs
Microchip TC74 thermal sensor

## Slide 9: Hardware
RA4
SWITCH

## Slide 10: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Hardware
------------PORTA---------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------------------ADC--
IO: ---------------------------------
------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
IO: ---------------------------------
------------PORTC----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: --------------------------------
IO: ---------------------------------
------------PORTD----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: --------------------------------
IO: ---------------------------------
------------PORTE----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------RST---------------
IO: ---------------------------------

## Slide 11: Time
The tutoral combines previous tutorials by using the Analog-to-Digital Converter (ADC) to control the speed of rotation.
  Where speed is a time delay
    us, 10us, ms, 10ms, s, m or h
    wait time unit
    wait 1 ms

## Slide 12: Analog-to-Digital
GCBASIC completes the initialisation
Create a variable to store the ADC results
Read the ADC
  GCBASIC makes the process easy via the ReadAD10()
  ReadAD10 returns a value of 0 to 1023
Wait for a time period based on returned ADC value
Set the LEDs
Do it again….

## Slide 13: Wait
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Time delays are sometimes key to the operation of a program
Read ADC 10 bit
( 0 – 1023 )

## Slide 14: Rotate with Carry
 | LEDD3 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 15: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 16: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 17: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 18: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 19: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 20: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 21: Carry Test
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Did it overflow ?
If C = 1 then .. Or other test condition
Read ADC 10 bit
( 0 – 1023 )

## Slide 22: Scale
Scale()
Scale transforms an existing value to a new value within a specified scale
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Read ADC

## Slide 23: Workshop
Read the ADC to set the LEDs
Uses
  A Byte variable
  Simple logic

## Slide 25: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, EEPROM and DATA blocks
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 26: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 4 – sequence the LEDs
January 2025