## Slide 1: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 7 – make the LEDs flash in a sequence with reverse

## Slide 2: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 7 – make the LEDs flash in a sequence with reverse
January 2025

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC16Fxxxx
PIC16Fxxxx is a high performance PIC16
  Digital and Analog peripherals
  8 –bit or 10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
The PIC16 offers 8, 14,18,20, 28, 40 and 48-pin packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, EEPROM and DATA blocks
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC supports the 16Fxxxx chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the PIC attached
  You have the 4 LEDs operating
  You have a POT connected
  You have switches connected

## Slide 8: Hardware
The PICDEM 2 Plus Demonstration Board
18-, 28- and 40-pin DIP sockets (although three sockets are provided, only one device may be used at a time)
On-board, +5V regulator for direct input from 9V, 100 mA AC/DC wall adapter or 9V battery, or hooks for a +5V, 100 mA regulated DC supply
RS-232 socket and associated hardware for direct connection to an RS-232 interface
Programmer/debugger connectivity supporting MPLAB® ICD 3, MPLAB REAL ICE, PICkit 2 and PICkit 3
PICkit Serial Connector for analysis of serial communications peripherals such as SPI or I2C™
5 k pot for devices with analog inputs
Three push button switches for external stimulus and Reset
Power-on indicator LED
Four LEDs connected to PORTB
On-board external oscillators including: a) Unpopulated DIP socket for canned crystal oscillator (Y2) b) RC oscillator circuit (R4, C3) c) Unpopulated holes for crystal connection (Y1) d) 32.768 kHz crystal for Timer1 clock operation (Y3)
32K x 8 Serial EEPROM
LCD display
Piezo buzzer
Prototype area for user hardware
Expansion Header for PICtail™ daughter card connectivity or user access to
MCUs
Microchip TC74 thermal sensor

## Slide 9: Hardware

## Slide 10: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Switches
Hardware
------------PORTA---------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ------------SW2-------------ADC--
IO: ---------------------------------
------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
IO: ---------------------------------
------------PORTC----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: --------------------------------
IO: ---------------------------------
------------PORTD----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: --------------------------------
IO: ---------------------------------
------------PORTE----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------RST---------------
IO: ---------------------------------

## Slide 11: Pulling it all together
Output
  LEDs rotating in sequence
Input
  Switch to control direction of sequence
  Using Master Clear as an input NOT as a reset
ADC
  Read the voltage from the potentiometer
Time
  Using WAIT that consistent across all mcu frequency

## Slide 12: Tutorial overview
Initialise
Do forever
  Read ADC
  Determine if switch state changed
  Set state of LEDs – left or right
  Wait
Loop
Initialise
Flash an LED
Wait
Set State of LEDS
Left
Right
Do Forever
Set State of LEDs
Switch state changed
ReadADC

## Slide 14: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, EEPROM and DATA blocks
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 15: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 7 – make the LEDs flash in a sequence with reverse