## Slide 1: GCBASIC Part 3
GCBASIC for the PIC18FxxQ20 chip Family
February 2024

## Slide 2: PIC18FxxQ20
PIC18-Q20 is a high performance PIC18
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI, I3C
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ20 offers 14- and 20-pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The GCBASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: GCBASIC Toolchain
GCBASIC
Toolchain
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ20 chip family

## Slide 5: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Hardware
-------------------PORTA---------------- Bit#: -7---6---5---4---3---2---1---0--- IO: ----------------------------ADC-- ----------------------------------------- -------------------PORTB---------------- Bit#: -7---6---5---4---3---2---1---0--- IO: --------------------------------- ----------------------------------------- ------------------PORTC----------------- Bit#: -7---6---5---4---3---2---1---0--- IO: LED-LED-LED-LED------------------ -----------------------------------------

## Slide 6: Analog-to-Digital
We configure the ADC, run a conversion, read the analog voltage controlled by the potentiometer on the board, and display the results on the LEDs.

## Slide 7: Analog-to-Digital
Using AN0 connected to RA0 (PortA.0)

## Slide 8: Analog-to-Digital
GCBASIC completes the initialisation
Create a variable to store the ADC results
Read the ADC
  GCBASIC makes the process easy via the ReadADC()
  ReadADC returns a value of 0 to 255
Set the LEDs
Do it again….

## Slide 9: Analog-to-Digital

## Slide 10: Lab
Examine the sample code
Review the results

## Slide 12: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The GCBASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 13: GCBASIC Part 3
GCBASIC for the PIC18FxxQ20 chip Family
February 2024

## Slide 14: Backup Slides

## Slide 15
Initialise
Create a variable
Read the ADC
ADC < 50
Yes
No
Set NO LEDS
ADC >50 <100
Yes
No
Set 1 LED
ADC >100
< 150
Yes
No
Set 2 LEDS
ADC >150
< 200
Yes
No
Set 3 LEDS
Set 4 LEDS