## Slide 1: GCBASIC Part 4
GCBASIC for the PIC18FxxQ20 chip Family
February 2024

## Slide 2: PIC18FxxQ20
PIC18-Q20 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI, I3C
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ20 offers 14- and 20-pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The GCBASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: GCBASIC Toolchain
GCBASIC
Toolchain
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ20 chip family

## Slide 5: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Potentiometer
Hardware
-------------------PORTA---------------- Bit#: -7---6---5---4---3---2---1---0--- IO: ----------------------------ADC-- ----------------------------------------- -------------------PORTB---------------- Bit#: -7---6---5---4---3---2---1---0--- IO: --------------------------------- ----------------------------------------- ------------------PORTC----------------- Bit#: -7---6---5---4---3---2---1---0--- IO: LED-LED-LED-LED------------------ -----------------------------------------

## Slide 6: Time
The tutoral combines previous tutorials by using the Analog-to-Digital Converter (ADC) to control the speed of rotation.
  Where speed is a time delay
    us, 10us, ms, 10ms, s, m or h
    wait time unit
    wait 1 ms

## Slide 7: Analog-to-Digital
GCBASIC completes the initialisation
Create a variable to store the ADC results
Read the ADC
  GCBASIC makes the process easy via the ReadAD10()
  ReadAD10 returns a value of 0 to 1023
Wait for a time period based on returned ADC value
Set the LEDs
Do it again….

## Slide 8: Wait
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Time delays are sometimes key to the operation of a program
Read ADC 10 bit
( 0 – 1023 )

## Slide 9: Lab
Examine the sample code
Review the results

## Slide 11: Scale
Scale
Scale transforms an existing value to a new value within a specified scale
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Read ADC

## Slide 12: Lab
Revise the sample code
Review the results

## Slide 14: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 15: GCBASIC Part 4
GCBASIC for the PIC18FxxQ20 chip Family
February 2024

## Slide 16: Backup Slides

## Slide 17
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes