## Slide 1: GCBASIC Part 5
GCBASIC for the PIC18FxxQ20 chip Family
February 2024

## Slide 2: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The GCBASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 3: PIC18FxxQ20
PIC18-Q20 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI, I3C
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ20 offers 14 and 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 4: GCBASIC Toolchain
GCBASIC
Toolchain
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ20 chip family

## Slide 5: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Potentiometer
Hardware
-------------------PORTA---------------- Bit#: -7---6---5---4---3---2---1---0--- IO: -----------------SW---------ADC-- ----------------------------------------- -------------------PORTB---------------- Bit#: -7---6---5---4---3---2---1---0--- IO: --------------------------------- ----------------------------------------- ------------------PORTC----------------- Bit#: -7---6---5---4---3---2---1---0--- IO: LED-LED-LED-LED------------------ -----------------------------------------

## Slide 7: Switch
The switch is connected RA3
When the switch is depressed RA3 will transition to 0v

## Slide 8: Tutorial overview
Initialise
Set LED off
Keypressed = TRUE
Initialise
Check the switch
  If pushed then toggle LED
  If not pushed then do it again
Checking the switch by using function to inspect the switch state
Loop
Toggle LED
No
Yes

## Slide 9: Lab
Review GCSTUDIO options
Examine the sample code
Review the results

## Slide 11: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 12: GCBASIC Part 5
GCBASIC for the PIC18FxxQ20 chip Family
February 2024

## Slide 13: Backup Slides

## Slide 14
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes