## Slide 1: GCBASIC Part 6
GCBASIC for the PIC18FxxQ20 chip Family
February 2024

## Slide 2: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The GCBASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 3: PIC18FxxQ20
PIC18-Q20 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI, I3C
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ20 offers 14 and 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 4: GCBASIC Toolchain
GCBASIC
Toolchain
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ20 chip family

## Slide 5: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Potentiometer
Switch
Hardware
-------------------PORTA---------------- Bit#: -7---6---5---4---3---2---1---0--- IO: -----------------SW---------ADC-- ----------------------------------------- -------------------PORTB---------------- Bit#: -7---6---5---4---3---2---1---0--- IO: --------------------------------- ----------------------------------------- ------------------PORTC----------------- Bit#: -7---6---5---4---3---2---1---0--- IO: LED-LED-LED-LED------------------ -----------------------------------------

## Slide 6: Using the Reset as input or Master Clear
The switch is connected RA3
The configuration switches control the operation of RA3
  MCRLE
    EXTMCRL - pin is MCLR
    INTMCRL - pin function is port defined function

## Slide 7: Tutorial overview
Initialise
Flash an LED
RSTButton = 0
Part 1 – RA3 as input
  Initialise
  Check the reset switch
    If pushed then toggle LED
Part 2 – RA3 as reset
  Initialise
  Resets every time…
Loop
Set LED State
No
Yes
Do Forever

## Slide 8: Lab
Examine the sample code
Review the results

## Slide 10: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – may the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 11: GCBASIC Part 6
GCBASIC for the PIC18FxxQ20 chip Family
February 2024

## Slide 12: Backup Slides

## Slide 13
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes