## Slide 1: Great Cow BASIC Part 11
Great Cow BASIC for the PIC18FxxQ41 chip Family
January 2021

## Slide 2: PIC18FxxQ41
PIC18-Q41 is a high performance PIC18
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
The PIC18xxQ41 offers 14- and 20-pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LED
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for PIC and AVR microcontrollers
Great Cow BASIC now supports the 18FxxQ41 chip family

## Slide 5: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf

## Slide 6: Hardware
Layout
By Chris Roper

## Slide 7: I2C
I2C uses two bidirectional open collector or open drain lines pulled up with resistors
  Serial Data Line (SDA)
  Serial Clock Line (SCL)
Typical voltages used are +5 V or +3.3 V, although systems with other voltages are permitted

## Slide 8: Hardware
Layout
TX
1. GND
4. I2C
Clock
3. I2C
Data
2. VCC

## Slide 9: Setup
CLOCK
DATA
VCC

## Slide 10: Lab
Examine the sample code
  Using PPS select the I2C ports
  Using PPS select the serial USART port
  Set up the I2C
  Review the code
  See the results

## Slide 12: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 13: Great Cow BASIC
Great Cow BASIC for the PIC18FxxQ41 chip Family
January 2021

## Slide 15: Backup Slides

## Slide 16: I2C