## Slide 1: Great Cow BASIC Part 19
Great Cow BASIC for the PIC18FxxQ41 chip Family
January 2021

## Slide 2: Tutorials...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 3: PIC18FxxQ41
PIC18-Q41 is a high performance PIC18
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
The PIC18xxQ41 offers 14- and 20-pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
Great Cow BASIC now supports the 18FxxQ41 chip family
Great Cow BASIC is a cross platform with common code translation

## Slide 5: The core compiler
Great Cow BASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
ASM file
Absolute Machine Code
HEX file
8 bit PIC and AVR
Reports:
TXT and HTML
Great Cow BASIC Compiler

## Slide 6: Using MPLAB-X
Great Cow BASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
file
Absolute Machine Code
HEX file
8 bit PIC and AVR
PIC-AS,
MPLAB-IDE
Reports:
TXT and HTML
Great Cow BASIC Compiler

## Slide 7: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf

## Slide 8: Lab
We will see two tests
Using the method used in the tutorials – PICKitPlus ( Pickit2 or Pickit3)
Using the PICkit4 method

## Slide 9: Resources
Tutorial source code
  https://github.com/Anobium/Great-Cow-BASIC-Demonstration-Sources/tree/master/Vendor_Boards/Microchip_Low_Pin_Count_Demo_Board/PICKit2_Board/18F16Q41
  Tutorial presentations
  https://github.com/Anobium/Great-Cow-BASIC-Demonstration-Sources/tree/master/Vendor_Boards/Microchip_Low_Pin_Count_Demo_Board/PICKit2_Board/18F16Q41/tutorials

## Slide 10: Summary
Great Cow BASIC supports the PIC18-Q41
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
Great Cow BASIC supports multiple 32/64 bit operating systems and integrates with MPLAB-X

## Slide 11: Great Cow BASIC
Great Cow BASIC for the PIC18FxxQ41 chip Family
January 2021