## Slide 1: Great Cow BASIC Part 8
Great Cow BASIC for the PIC18FxxQ41 chip Family
January 2021

## Slide 2: PIC18FxxQ41
PIC18-Q41 is a high performance PIC18
  Digital and Analog peripherals
  12-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
The PIC18xxQ41 offers 14- and 20-pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LED
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 4: Great Cow BASIC Compiler
Great Cow BASIC Compiler
Great Cow BASIC is an Open Source compiler for PIC and AVR microcontrollers
Great Cow BASIC now supports the 18FxxQ41 chip family

## Slide 5: Hardware
Microchip Low Pin Count Demo Board
PICKit_2_Low_Pin_Count_User_Guide_51556a.pdf

## Slide 6: Hardware
Layout
By Chris Roper
TX
GND

## Slide 7: Serial output
Output
  Using the built-in Universal Synchronous/Asynchronous Receiver Transmitter (USART) on the PIC® Microcontroller to communicate with serial termial on a PC
Baseline is the tutorial we have been using plus a TTL/USB serial converter

## Slide 8: Serial output
GND and RX (RXD)

## Slide 9: Peripheral Pin Select (PPS)
PPS configuration provides the method to these choices set the functionality and their placement on a wide range of I/O pins.
By increasing the pinout options available on a particular device, users can tailor the device to their entire application.
However for Serial we must set the TX using PPS

## Slide 10: Tutorial overview
Initialise
Serial up the serial
Initialise
Do forever
  Read ADC
  Determine if switch state changed
  Set state of LEDs
  Wait
Loop
Wait
Set State of LEDS
Left
Right
Do Forever
Set State of LEDs
Switch state changed
Send Values to Serial
ReadADC

## Slide 11: Lab
Examine the sample code
Review the results

## Slide 13: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using CCP/PWM to dim the LEDS
Using I2C with serial to discover I2C devices
Using EEProm – showing values on the serial terminal
Using an I2C GCLD display
Using an SPI GCLD display
Using PWM to dim the LEDS
Using memory within the PIC – Progmem and SAF memory
The Great Cow BASIC tool chain
Assembly and alternatives assemblers
Summary

## Slide 14: Great Cow BASIC
Great Cow BASIC for the PIC18FxxQ41 chip Family
January 2021

## Slide 16: Backup Slides

## Slide 17
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes

## Slide 18: Analog-to-Digital