## Slide 1: GCBASIC
18FXXQ24 CHIPFAMILY

## Slide 2: GCBASIC 18FxxQ24
November 2024 release
GCBASIC
New chip family
The I2C challenge

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 4: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ24 chip family
GCBASIC is a cross platform with common code translation

## Slide 5: The core compiler
GCBASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
ASM file
Absolute Machine Code
HEX file
8 bit PIC, AVR, AVR-DX and LGT
Reports:
TXT and HTML
GCBASIC Compiler
Chip Specific DAT file
Chip Specific Constraints
HWI2C.h
I2C.h

## Slide 6: Hardware
GCBASIC prototype board
  8, 14, 18, 28 and 40 pin devices
  LEDs
  Switches
  POTs
  Connections
    USB, GLCD, LCD
    Sensors
PICKit2 using PICKitPlus
External power supply
USART/TTL adapter
I2C Device attached correctly

## Slide 7: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Switches & resistors
I2C device
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------SW----------ADC--
----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
----------------------------------------
------------------PORTC-----------------
Bit#: -X---6---5---4---3---2---1---0---
IO: -^--TX------SCL-SDA--------------
-----VDDIO2-----------------------------
You must apply correct Voltage
------------------PORTE-----------------
Bit#: -----------------3---------------
IO: ----------------SW---------------

## Slide 8
Hardware Power Domain

## Slide 9: Setup
CLOCK
---------
SCL
DATA
---------
SDA
VCC

## Slide 10: I2C

## Slide 12: LAB
Demonstrate I2C working to show i2c results on a terminal
  Hardware i1c – hwi2c.h
    Using PPS select the I2C ports
    Set up the I2C
    See the results
  Test 1 – Inline test with no GCBASIC I2C library
  Test 2 – Basic operations test with GCBASIC I2C library
  Test 3 – I2C discovery with GCBASIC I2C library
  Test 4 –I2C GLCD operations

## Slide 13: Summary findings
DAT memory specification section ( ‘[FreeRAM]’ ) was incorrect - resolved
  [FreeRAM] RAM location – fixed within GETCHIPDATA.BAS
  ADC initially shows no results
  Wrong connection on the test rig!
EEPROM demo program not working as expected
  EEPROM/H required updating
PPSTOOL does not support Q24
  Edit XML to represent this new family
Issue Noted
  Compiler does not handle undefined port.bit appropriate portc.7

## Slide 14: GCBASIC 18FxxQ24
November 2024 release
GCBASIC
Like and subscribe!
New chip family – getting the basics operating