## Slide 1: GCBASIC
PIC18FxxQ24
Part 16 - Progmem, SAF memory, EEPROM and DATA blocks

## Slide 2: GCBASIC
PIC18FxxQ24
Part 16 - Progmem, SAF memory, EEPROM and DATA blocks

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC18FxxQ24
PIC18-Q24 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ24 offers 28, 40 and 48-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC and AVR microcontrollers
GCBASIC now supports the 18FxxQ24 chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 18FxxQ24 attached
  You have the 4 LEDs operating
  You have a POT connected
  You have SWITCHes connected
  You have a USB/TTL converter

## Slide 8: Power Domain – VDDIO2

## Slide 9: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Switches & resistors
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------SW----------ADC--
----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
----------------------------------------
------------------PORTC-----------------
Bit#: -X---6---5---4---3---2---1---0---
IO: -^--TX---------------------------
-----VDDIO2-----------------------------
You must apply correct Voltage
------------------PORTE-----------------
Bit#: -----------------3---------------
IO: ----------------SW---------------

## Slide 10: Storage Overview Types
 | Type | Characteristics
1 | Progmem | Program, and, Storage Area Flash (SAF) block
2 | Data RAM | Volatile
3 | Data EEPROM | Consider as a peripheral
SAF

## Slide 11: Progmem
or
Progmem usage
  Your program
  and/or
  Reference data
  Pictures
Uses PFM direct addressing
Program
Program Flash Memory
( 32 KW )
PIC18FxxQ24
Program
Program Flash Memory
( 32 KW )
PIC18FxxQ24

## Slide 12: Progmem
or
Progmem usage
  Your program
  and/or
  Reference data
  Pictures
Uses PFM direct addressing
Program
Reference Data
Program Flash Memory
( 32 KW )
PIC18FxxQ24
Program
Reference Data
Program Flash Memory
( 32 KW )
PIC18FxxQ24

## Slide 13: SAF
SAF usage
  Reference data
  Must not be overwritten by user program – you MUST adjust program to NOT use SAF block
Uses SAF offset addressing
or
Program
SAF Data
Program Flash Memory
( 32 KW )
PIC18FxxQ24
Program
SAF Data
Program Flash Memory
( 32 KW )
PIC18FxxQ24
SAF is designated for storing non-volatile data and can be protected to ensure data integrity and security.

## Slide 14: Progmem
or
Progmem usage
  Your program
  and/or
  Reference data
  Pictures
Uses PFM direct addressing
Program
Reference Data
Program Flash Memory
( 32 KW )
PIC18FxxQ24
Program
Reference Data
Program Flash Memory
( 32 KW )
PIC18FxxQ24

## Slide 15: EEDATA & DATA Blocks
 | Type | Characteristics
1 | EEDATA | An EEPROM block or blocks of data that is programmed into the EEPROM
2 | DATA | An DATA block or blocks of data that is programmed just above your program
Both areas can be easily used for reference data

## Slide 16: Lab
Walk the examples
  PROGMEM
  SAF
  EEPROM and DATA blocks

## Slide 18: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 19: GCBASIC
PIC18FxxQ24
Part 16 - Progmem, SAF memory, EEPROM and DATA blocks