## Slide 1: GCBASIC
PIC18FxxQ24
Part 10 - EEPROM Operations

## Slide 2: GCBASIC
PIC18FxxQ24
Part 10 - EEPROM Operations

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC18FxxQ24
PIC18-Q24 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ24 offers 28, 40 and 48-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC and AVR microcontrollers
GCBASIC now supports the 18FxxQ24 chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 18FxxQ24 attached
  You have the 4 LEDs operating
  You have a POT connected
  You have SWITCHes connected
  You have a USB/TTL converter

## Slide 8: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Switches & resistors
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------SW----------ADC--
----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
----------------------------------------
------------------PORTC-----------------
Bit#: -X---6---5---4---3---2---1---0---
IO: -^--TX---------------------------
-----VDDIO2-----------------------------
You must apply correct Voltage
------------------PORTE-----------------
Bit#: -----------------3---------------
IO: ----------------SW---------------

## Slide 9: Power Domain – VDDIO2

## Slide 10: Memory
64 KB of Program Flash Memory
4 KB of Data SRAM Memory
512 Bytes Data EEPROM
Memory Access Partition, the Program Flash Memory Can Be Partitioned into:
  Application Block
  Boot Block
  Storage Area Flash (SAF) Block

## Slide 11
EEProm
Electrically Erasable Programmable Read-Only Memory
Non-volatile memory to store relatively small amounts of data but allowing individual bytes to be erased and reprogrammed.

## Slide 12: EEProm
Type Value Explanation
Prog 32768 Prog is exposed as ChipWORDS
SAFMemWords 128 SAFMemWords exposed ChipSAFMemWords
EEPROM 512 EEPROM is exposed as ChipEEPROM
RAM 4096 RAM is exposed as ChipRAM

## Slide 13: EEProm – 3 ways

## Slide 14: Lab
Sample code – write and read via terminal
  Using PPS select the serial USART port
  Write values to EEProm
  Read values to EEProm
  See the results on terminal
Sample code – write with read via programmer
  Write values to EEProm
  See the results within PICKitPlus
Sample code – check the chip specific constant
  See the results on terminal

## Slide 16: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 17: GCBASIC
PIC18FxxQ24
Part 10 - EEPROM Operations