## Slide 1: GCBASIC
PIC18FxxQ24
Part 13 - Using a SPI GLCD display solutions

## Slide 2: GCBASIC
PIC18FxxQ24
Part 13 - Using a SPI GLCD display solutions

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC18FxxQ24
PIC18-Q24 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ24 offers 28, 40 and 48-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC and AVR microcontrollers
GCBASIC now supports the 18FxxQ24 chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 18FxxQ24 attached
  You have the 4 LEDs operating
  You have a POT connected
  You have SWITCHes connected
  You have a USB/TTL converter
  GLCD SPI device

## Slide 8: Power Domain – VDDIO2

## Slide 9: SPI
Serial Peripheral Interface (SPI) is an interface bus commonly used to send data between microcontrollers and small peripherals such as GLCD, shift registers, sensors, and SD cards.
It uses separate clock and data lines, along with a select line to choose the device you wish to control.

## Slide 10: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Switches & resistors
SPI device and circuit
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------SW----------ADC--
----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
----------------------------------------
------------------PORTC-----------------
Bit#: -X---6---5---4---3---2---1---0---
IO: -^--TX------SDO-SCK-RST--CS--DC--
-----VDDIO2-----------------------------
You must apply correct Voltage
------------------PORTE-----------------
Bit#: -----------------3---------------
IO: ----------------SW---------------

## Slide 11: Setup - Connections

## Slide 12: Setup - Program
DATA
This is a PPS chip, so, needs to make the PPS match these assignments
#DEFINE GLCD_DO portC.4
#DEFINE GLCD_SCK portC.3
'Pin mappings for GCLD
#DEFINE GLCD_DC portC.0
#DEFINE GLCD_CS portC.1
#DEFINE GLCD_RESET portC.2
SPI GLCD
GCBASIC

## Slide 13: Setup – when things do not work ..
Things do not always work
  The more connections the more trouble
Things we know
  The GLCD demonstration works
  Therefore is not likely to be the libraries but … work through the checklist first
Checklist
  Check your connections, twice
  Write a program to pulse a signal on each line, each line on at a time
  Always use the software SPI first to prove connectivity
  Then, use PPS/hardware SPI is #2 works

## Slide 15: Lab
Review setup and operation of a SPI GLCD
  Software SPI – bit banging
  Harware SPI – with PPS ( of course)
    Conditional compilation

## Slide 16: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 17: GCBASIC
PIC18FxxQ24
Part 13 - Using a SPI GLCD display solutions