## Slide 1: GCBASIC
PIC18FxxQ24
Part 14 - PMW many ways

## Slide 2: GCBASIC
PIC18FxxQ24
Part 14 - PMW many ways

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC18FxxQ24
PIC18-Q24 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ24 offers 28, 40 and 48-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC and AVR microcontrollers
GCBASIC now supports the 18FxxQ24 chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 18FxxQ24 attached
  You have the 4 LEDs operating
  You have a POT connected
  You have SWITCHes connected
  You have a USB/TTL converter

## Slide 8: Power Domain – VDDIO2

## Slide 9: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Switches & resistors
SPI device and circuit
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------SW----------ADC--
----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
----------------------------------------
------------------PORTC-----------------
Bit#: -X---6---5---4---3---2---1---0---
IO: -^--TX---------------------------
-----VDDIO2-----------------------------
You must apply correct Voltage
------------------PORTE-----------------
Bit#: -----------------3---------------
IO: ----------------SW---------------

## Slide 11: Pulse Width Modulation
Pulse Width Modulation ( PWM ) is simply a succession of pulses – is a method of reducing the average power delivered by an electrical signal, by effectively chopping it up into discrete parts.
The average value of voltage (and current) fed to the load is controlled by turning on and off at a fast rate. The longer the signal is on compared to the off periods, the higher the total power supplied to the load.

## Slide 12: PWM

## Slide 13: Setup
http://www.gabotronics.com/development-boards/xmega-xminilab.htm

## Slide 14: PWM
 | PWM type | Characteristics | PPS required | Comment
1 | The simplest way | Port on and off | No | Any port**
2 | The pulseout() way | PulseOut() a port for a period | No | Any port**
3 | The PWMOut() way | PWMOUT() a number of pulses | No | Any port**
4 | CCP/PWM way | Fixed frequency, fixed duty using timer2* | Yes – CCP/PWMx module | Low code impact, two constants
5 | CCP/PWM way | Variable frequency, variable duty using timer2* | Yes – CCP/PWMx module | ASM does the heavy lifting
6 | PWM 16 bit way | Wide range of capabilities | Yes - PWMxx | Lots of parameters
7 | Timer interrupt way | Use a timer1* | No | Any port**
* could use other timers
** any valid output

## Slide 15: Lab
Walk the examples
View the scope

## Slide 17: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 18: GCBASIC
PIC18FxxQ24
Part 14 - PMW many ways