## Slide 1: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 3 – Using the ADC

## Slide 2: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 3 – Using the ADC
January 2025

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC16Fxxxx
PIC16Fxxxx is a high performance PIC16
  Digital and Analog peripherals
  8 –bit or 10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
The PIC16 offers 8, 14,18,20, 28, 40 and 48-pin packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, EEPROM and DATA blocks
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC supports the 16Fxxxx chip family

## Slide 7: Basic setup and flash the LED
Installed the GCBASIC software
Installed your programmer software
Test that you have the 16Fxxxx attached
Tutorial #1 has been completed

## Slide 8: Hardware
The PICDEM 2 Plus Demonstration Board
18-, 28- and 40-pin DIP sockets (although three sockets are provided, only one device may be used at a time)
On-board, +5V regulator for direct input from 9V, 100 mA AC/DC wall adapter or 9V battery, or hooks for a +5V, 100 mA regulated DC supply
RS-232 socket and associated hardware for direct connection to an RS-232 interface
Programmer/debugger connectivity supporting MPLAB® ICD 3, MPLAB REAL ICE, PICkit 2 and PICkit 3
PICkit Serial Connector for analysis of serial communications peripherals such as SPI or I2C™
5 k pot for devices with analog inputs
Three push button switches for external stimulus and Reset
Power-on indicator LED
Four LEDs connected to PORTB
On-board external oscillators including: a) Unpopulated DIP socket for canned crystal oscillator (Y2) b) RC oscillator circuit (R4, C3) c) Unpopulated holes for crystal connection (Y1) d) 32.768 kHz crystal for Timer1 clock operation (Y3)
32K x 8 Serial EEPROM
LCD display
Piezo buzzer
Prototype area for user hardware
Expansion Header for PICtail™ daughter card connectivity or user access to
MCUs
Microchip TC74 thermal sensor

## Slide 9: Analog-to-Digital
We configure the ADC, run a conversion, read the analog voltage controlled by the potentiometer on the board, and display the results on the LEDs.

## Slide 10: Analog-to-Digital

## Slide 11: Analog-to-Digital
GCBASIC completes the initialisation
Create a variable to store the ADC results
Read the ADC
  GCBASIC makes the process easy via the ReadADC()
  ReadADC returns a value of 0 to 255
Set the LEDs
Do it again….

## Slide 12: Analog-to-Digital

## Slide 13: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the PIC attached
  You have the 4 LEDs operating
  You have a POT connected

## Slide 14: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Hardware
------------PORTA---------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------------------ADC--
IO: ---------------------------------
------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
IO: ---------------------------------
------------PORTC----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: --------------------------------
IO: ---------------------------------
------------PORTD----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: --------------------------------
IO: ---------------------------------
------------PORTE----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------RST---------------
IO: ---------------------------------

## Slide 15: Workshop
Read the ADC to set the LEDs
Uses
  A Byte variable
  Simple logic

## Slide 17: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, EEPROM and DATA blocks
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 18: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 3 – Using the ADC