## Slide 1: GCBASIC
Compiler Control - #STARTUP

## Slide 2: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports 1400+ controllers
GCBASIC is a cross platform with common code translation

## Slide 3: The core compiler
GCBASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
ASM file
Absolute Machine Code
HEX file
8 bit PIC, AVR, AVR-DX and LGT
Reports:
TXT and HTML
GCBASIC Compiler
Chip Specific DAT file
Chip Specific Constraints

## Slide 4: Concept of Operations
The #startup directive in GCBASIC allows for executing a routine immediately after system initialization.
Key Features:
  Initial Setup: Defines a subroutine that executes during the startup phase.
  Configuration: Used for setting up configurations and initializing variables.
  Automation: Ensures necessary initializations are automatically handled at startup.
Benefits:
  Streamlined Code: Reduces the need for manual initialization in the main program.
  Efficiency: Improves system performance by ensuring all essential setups are completed before the main execution.
  Readability: Enhances code readability by separating initialization code from the main program logic.

## Slide 5: Concept of Operations
Source Code
Libraries
#startup SubName [, priority]
Explanation:
#startup is used in include files to automatically insert initialization routines. If a DEFINE or subroutine from the file is used in the program, then the specified subroutine will be called.
The priority to #startup support the setting of the priority of the subroutines for all the libraries in a project.
Subroutines will be called in order from smallest to largest priority number.
Source and libraries files can contain many, many routines like SUBs and Functions
Each source file may have only ONE #startup SUB

## Slide 6: Concept of Operations
Source Code
Libraries
LCD.H
#startup INITLCD
USER PROGRAM
#startup PPSInit, 85

## Slide 7: My eBay purchase

## Slide 8: However….in practice
You have a new LCD
  The GCBASIC LCD routines fail to initialise
  You want to write your own LCD initialise routine, but you want to ensure the GCBASIC standard INITLCD() does not operate before your own LCD initialise routine
  How to do this?
You want to write your own INITSYS routine.
  You can add your own routine to initialise the microntroller but the default INITSYS would always be called in the ASM.
  How to do this?

## Slide 9: Schematic

## Slide 10: Compiler controls
The compiler now supports the updating of the #startup(s) with your own routines, or even to cancel #startup(s).
  The compiler will search for all #startup(s) and update across all sources (libraries and includes). LCD.H is just an example.
#DEFINE INITLCD myINITLCD
  This will change any reference in the LCD.h #startup INITLCD to #startup myINITLCD.
#DEFINE INITLCD
  With no second parameter would cancel any #startup in LCD.h.
#DEFINE INITSYS myINITSYS
  This will change the default INITSYS to myINITSYS.
#DEFINE INITSYS
  This will remove the INITSYS from the initialisation of the microcontroller.

## Slide 11: Lab

## Slide 12: Summary
These new compiler controls give greater flexibility to improve and ease the development of solutions.

## Slide 13: GCBASIC
Compiler Control - #STARTUP