## Slide 1: GCBASIC
PIC18FxxQ35chip Family
Part 12 - GLCD Operations using I2C

## Slide 2: GCBASIC
PIC18FxxQ35chip Family
Part 12 - GLCD Operations using I2C

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC18FxxQ35
PIC18FxxQ35 is a high performance PIC18
  Digital and analog peripherals for flexible embedded control
  10-bit ADC for accurate analog signal conversion
  Multiple communication interfaces including UART (serial), I²C, and SPI
  PWM modules with CCP and 16-bit resolution for precise timing and motor control
  Configurable Logic Cells (CLCs) for custom hardware-level logic without external components
  Integrated op amps for onboard analog signal conditioning and amplification
The PIC18FxxQ35 offers 28, 40 and 44-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ35 chip family
GCBASIC now supports 1400+ microcontrollers

## Slide 7
PICDEM 2 Plus Demonstration
Board
1. 18-, 28- and 40-pin DIP sockets
(although three sockets are provided, only one device may be used at a time)
2. On-board, +5V regulator for direct input from 9V, 100 mA AC/DC wall adapter or 9V battery, or hooks for a +5V, 100 mA regulated DC supply
3. RS-232 socket and associated hardware for direct connection to an RS-232 interface
4. Programmer/debugger connectivity supporting MPLAB® ICD 3, MPLAB REAL ICE and PICkitPlus
5. PICkit Serial Connector for analysis of serial communications peripherals such as SPI or I2C™
6. 5 k pot for devices with analog inputs
7. Three push button switches for external stimulus and Reset
8. Power-on indicator LED
9. Four LEDs connected to PORTB
10. On-board external oscillators including:
a) Unpopulated DIP socket for canned crystal oscillator (Y2)
b) RC oscillator circuit (R4, C3)
c) Unpopulated holes for crystal connection (Y1)
d) 32.768 kHz crystal for Timer1 clock operation (Y3) 11. 32K x 8 Serial EEPROM
12. LCD display
13. Piezo buzzer
14. Prototype area for user hardware
15. Expansion Header for PICtail™ daughter card connectivity or user access to MCU pins
16. Microchip TC74 thermal sensor
Plus I2C GLCD
3A

## Slide 8
PICDEM 2 Plus Demonstration
Board

## Slide 9: Schematic

## Slide 10: VDDIO2 Domain Power
Think No VDDIO2 power – no domain I/O!

## Slide 11: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 18FxxQ35 attached
  You have the 4 LEDs operating
  You have a POT connected
  You have SWITCHes connected
  You have a USB/TTL converter
  GLCD i2C device and i2c discovery has worked!

## Slide 12: I2C
I2C uses two bidirectional open collector or open drain lines pulled up with resistors
  Serial Data Line (SDA)
  Serial Clock Line (SCL)
Typical voltages used are +5 V or +3.3 V, although systems with other voltages are permitted

## Slide 13: Setup
CLOCK
---------
SCL
DATA
---------
SDA
VCC

## Slide 14: I2C sequence
i2cStart
i2cSend Address
i2cSend
Data
i2cStop
Start Condition:
  Indicated by a high-to-low transition on the SDA line while SCL is high.
  This signals the beginning of communication.
Send (Address):
  Master sends the address of the slave device including by the Read/Write bit.
  Slave responds with an Acknowledgment (ACK) bit.
Send (Data):
  Master sends or receives data bytes.
  Each byte is followed by an Acknowledgment (ACK) from the receiver.
Stop Condition:
  Indicated by a low-to-high transition on the SDA line while SCL is high.
  This signals the end of communication.

## Slide 15: I2C

## Slide 16
r
r
User Program
Libraries – 125+
Lowlevel – 25+
User Functions
Microcontroller specific solution (.HEX)
Converters
External Sources
DB, BMP, Version control…
7 segment, GLCD, Maths…
USART, I2C, SPI….

## Slide 17: Lab
Examine the sample code
  Using PPS select the I2C ports
  Using PPS select the serial USART port
  Set up the I2C
  Review demonstrations and see the results
Focus | Shows
64x32, 128x32 & 128x64 capability demos | Primitives Memory usage & Transactions
BMP converter | Converter
Sprite | Expose buffer and custom I2C subroutine
Voltmeter | Trig2places & Low level GLCD commands

## Slide 19: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display solutions
Using SPI GCLD display solutions
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 20: GCBASIC
PIC18FxxQ35chip Family
Part 12 - GLCD Operations using I2C