## Slide 1: GCBASIC
PIC18FxxQ35chip Family
Part 6 – Using the reset switch

## Slide 2: GCBASIC
PIC18FxxQ35 chip Family
Part 6 – Using the reset switch

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC18FxxQ35
PIC18FxxQ35 is a high performance PIC18
  Digital and analog peripherals for flexible embedded control
  10-bit ADC for accurate analog signal conversion
  Multiple communication interfaces including UART (serial), I²C, and SPI
  PWM modules with CCP and 16-bit resolution for precise timing and motor control
  Configurable Logic Cells (CLCs) for custom hardware-level logic without external components
  Integrated op amps for onboard analog signal conditioning and amplification
The PIC18FxxQ35 offers 28, 40 and 44-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ35 chip family
GCBASIC now supports 1400+ microcontrollers

## Slide 7
PICDEM 2 Plus Demonstration
Board
1. 18-, 28- and 40-pin DIP sockets
(although three sockets are provided, only one device may be used at a time)
2. On-board, +5V regulator for direct input from 9V, 100 mA AC/DC wall adapter or
9V battery, or hooks for a +5V, 100 mA regulated DC supply
3. RS-232 socket and associated hardware for direct connection to an RS-232
interface
4. Programmer/debugger connectivity supporting MPLAB® ICD 3, MPLAB REAL
ICE and PICkit 3
5. PICkit Serial Connector for analysis of serial communications peripherals such
as SPI or I2C™
6. 5 k pot for devices with analog inputs
7. Three push button switches for external stimulus and Reset
8. Power-on indicator LED
9. Four LEDs connected to PORTB
10. On-board external oscillators including:
a) Unpopulated DIP socket for canned crystal oscillator (Y2)
b) RC oscillator circuit (R4, C3)
c) Unpopulated holes for crystal connection (Y1)
d) 32.768 kHz crystal for Timer1 clock operation (Y3) 11. 32K x 8 Serial EEPROM
12. LCD display
13. Piezo buzzer
14. Prototype area for user hardware
15. Expansion Header for PICtail™ daughter card connectivity or user access to
MCU pins
16. Microchip TC74 thermal sensor

## Slide 8
PICDEM 2 Plus Demonstration
Board

## Slide 9: Schematic

## Slide 10: Using the Reset as input or Master Clear
RE3 Pin Functionality Overview
  RE3 is a multifunctional pin on certain PIC microcontrollers.
  It can operate either as a digital input or as a Master Clear (reset) signal.
🔧 Configuration Control via MCRLE Register
  EXTMCLR: External Master Clear enabled → RE3 functions as MCLR (reset input)
  INTMCLR: Internal Master Clear enabled → RE3 functions as digital input (e.g., switch)
🧠 Design Implications
  Choose EXTMCLR for hardware reset capability.
  Choose INTMCLR to repurpose RE3 for input tasks like button detection.

## Slide 11: Tutorial overview
Part 1 – RE3 as input
  Initialise
  Check the reset switch
    If pushed then toggle LED
Part 2 – RE3 as reset
  Initialise
  Resets every time…
Initialise
Flash an LED
RSTButton = 0
Loop
Set LED State
No
Yes
Do Forever

## Slide 12: Lab
Review PICINFO options
Examine the sample code
Review the results

## Slide 14: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 15: GCBASIC
PIC18FxxQ35 chip Family
Part 6 – Using the reset switch