## Slide 1: GCBASIC
PIC16F175xx
Part 13 - Using a SPI GLCD display solutions

## Slide 2: GCBASIC
PIC16F175xx
Part 13 - Using a SPI GLCD display solutions

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC16F175xx
PIC16165xx is a high performance PIC16
  Digital and analog peripherals for flexible embedded control
  10-bit ADC for accurate analog signal conversion
  Multiple communication interfaces including UART (serial), I²C, and SPI
  PWM modules with CCP and 16-bit resolution for precise timing and motor control
  Configurable Logic Cells (CLCs) for custom hardware-level logic without external components
  Integrated op amps for onboard analog signal conditioning and amplification
The PIC16175xx offers 14, 20, 28, 40 and 44-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC , AVR and LGT microcontrollers
GCBASIC now supports the 16F175xx chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 16F175xx attached
  You have the 4 LEDs operating
  You have a POT connected
  You have SWITCHes connected
  You have a USB/TTL converter
  GLCD SPI device

## Slide 8: SPI
Serial Peripheral Interface (SPI) is an interface bus commonly used to send data between microcontrollers and small peripherals such as GLCD, shift registers, sensors, and SD cards.
It uses separate clock and data lines, along with a select line to choose the device you wish to control.

## Slide 9: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Switches & resistors
SPI device and circuit
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------SW----------ADC--
----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ---------------------------------
----------------------------------------
------------------PORTC-----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----TX1-SDO-SCK-----RST--CS--DC—
-----------------------------------------
------------------PORTE-----------------
Bit#: -----------------3---------------
IO: ----------------MCLR--------------

## Slide 10: Setup - Connections

## Slide 11: Setup - Program
DATA
This is a PPS chip, so, needs to make the PPS match these assignments
/* Pin mappings for GLCD data and clock
#DEFINE GLCD_DO portC.5
#DEFINE GLCD_SCK portC.4
/* Pin mappings for GLCD support
#DEFINE GLCD_DC portC.0
#DEFINE GLCD_CS portC.1
#DEFINE GLCD_RESET portC.2 #DEFINE SSD1331_HardwareSPI
SPI GLCD
GCBASIC

## Slide 12: Setup – when things do not work ..
Things do not always work
  The more connections the more trouble
Things we know
  The GLCD demonstration works
  Therefore is not likely to be the libraries but … work through the checklist first
Checklist
  Check your connections, twice
  Write a program to pulse a signal on each line, each line on at a time
  Always use the software SPI first to prove connectivity
  Then, use PPS/hardware SPI is #3 works

## Slide 13: Lab
Review setup and operation of a SPI GLCD
  Software SPI – bit banging
  Harware SPI – with PPS ( of course)
    Conditional compilation

## Slide 15: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 16: GCBASIC
PIC16F175xx
Part 13 - Using a SPI GLCD display solutions