## Slide 1: GCBASIC
PIC16F175xx
Part 18 - The GCBASIC Tool Chain

## Slide 2: GCBASIC
PIC16F175xx
Part 18 - The GCBASIC Tool Chain

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 5: PIC16F175xx
PIC16175xx is a high performance PIC16
  Digital and analog peripherals for flexible embedded control
  10-bit ADC for accurate analog signal conversion
  Multiple communication interfaces including UART (serial), I²C, and SPI
  PWM modules with CCP and 16-bit resolution for precise timing and motor control
  Configurable Logic Cells (CLCs) for custom hardware-level logic without external components
  Integrated op amps for onboard analog signal conditioning and amplification
The PIC16175xx offers 14, 20, 28, 40 and 44-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 16F175xx chip family
GCBASIC is a cross platform with common code translation

## Slide 7: The Windows IDEs
GCBASIC Compiler
GCBASIC IDE
GC Studio
Programmers
PPSTool
AVRInfo
CLC
PicInfo
PSMC
Terminal
Program Editor
https://gcbasic.com/

## Slide 9: Tool chain
APPLICATION TITLE | CLASS | CORE | OS | SEEN | MAINTAINED
GCBASIC compiler | Compiler/Linker | Y | Windows, Linux, BSD, MAC | Y | Yes by GCBASIC team
Great Cow Graphical BASIC IDE | IDE/Compiler/Linker | y | Windows | N | Yes by GCBASIC team
AVRInfo | Code Generator | n | Windows, Linux, BSD, MAC | Y | Yes by GCBASIC team
AVRDude | Programmer | n | - | Y | http://savannah.nongnu.org\projects\avrdude
CLC Designer | Code Generator | n | Windows | Y | No
Converters | Converter | y | Windows, Linux, BSD, MAC | Y | Yes by GCBASIC team
CoolTerm | Terminal | n | Windows | N | Yes, see website
DFU Bootloader | Programmer | n | Windows, Linux, BSD, MAC | N | Anobium..GITHub
GC Code | IDE | y | Windows | Y | Yes by GCBASIC team
GC Studio | IDE | y | Windows | Y | Yes by GCBASIC team
G+Stool | Management Supervisor | y | Windows | Y | Yes by GCBASIC team
K150 | Programmer | n | Windows | N | http://www.kitsrus.com/pic.html
Micronucleus | Programmer | n | - | N | Micronucleus..GitHub
Northern Software | Programmer | n | Windows, Linux, BSD, MAC | Y | https://www.northernsoftware.com/
PICInfo | Code Generator | n | Windows, Linux, BSD, MAC | Y | Yes by GCBASIC team
PicKit2 command line – for older chips | Programmer | n | Windows, Linux | N | Microchip website
PicKit2 GUI – for older chips | Programmer | n | Windows | N | Microchip website
PicKit3 GUI – for older chips | Programmer | n | Windows | N | Microchip Website
PicKit3 MPLAB-IPE integration tool | Programmer | n | Windows, Linux | N | http://www.autoitscript.com
PICKitPlus – PICkit2 and PICKit3 suite | Programmer | n | Windows, Linux | Y | www.pickitplus.co.uk
PICPgm | Programmer | n | Windows | N | http://picpgm.picprojects.net/
PPS Tool | Code Generator | y | Windows | Y | Yes by GCBASIC team
Programmer editor | IDE | y | Windows | Y | Yes by GCBASIC team
PSMC Designer | Code Generator | n | Windows | N | No
Putty | Terminal | n | Windows | N | Yes, see website
SynWrite IDE | IDE | y | Windows | Y | Yes by GCBASIC team
Terminal | Terminal | n | Windows | Y | Yes, see website
TinyBootLoader | Programmer | n | Windows | N | http://tinypicbootload.sourceforge.net/
XpressLoader for Microchip Xpress boards | Programmer | n | Windows | N | https://sourceforge.net/p/gcbasic/code/HEAD/tree/utils/
MPLAB_IPE | Programmer | n | Windows, Linux | Y | https://www.microchip.com/mplab/mplab-x-ide
GCASM | Compiler/Linker | Y | Windows, Linux, BSD, MAC | Y | Yes by GCBASIC team
PIC-AS | Linker | n | Windows, Linux, BSD, MAC | Y | https://www.microchip.com/mplab/mplab-x-ide
MPASM | Linker | n | Windows, Linux, BSD, MAC | Y | https://www.microchip.com/mplab/mplab-x-ide
GPASM | Linker | n | Windows, Linux, BSD, MAC | Y | https://www.microchip.com/mplab/mplab-x-ide

## Slide 10: The core compiler
GCBASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
ASM file
Absolute Machine Code
HEX file
8 bit PIC, AVR, AVR-DX and LGT
Reports:
TXT and HTML
GCBASIC Compiler

## Slide 11: Compiler options
GCBASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
file
Absolute Machine Code
HEX file
PIC-AS, MPASM,
MPLAB-IDE,
GPASM, AVRASM2
Reports:
TXT and HTML
GCBASIC Compiler
8 bit PIC, AVR, AVR-DX and LGT

## Slide 12: Debugger options
GCBASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
High Level Language
Assembly Language
file
Simulator or
Absolute Machine Code
HEX file
GC CODE DEBUGGER ------------- PIC-AS
Reports:
TXT and HTML
GCBASIC Compiler
8 bit PIC

## Slide 13: The Variants for Linux, BSD & Mac
GCBASIC Compiler
An Editor
Scripts
Programmers
$ time LC_ALL=C /opt/GCBASIC/makehex.sh code9.gcb GCBASIC (0.98.07 RC07 2020-04-01 (Linux 64 bit)) Compiling code9.gcb ... Done Assembling program ... Program assembled successfully! real 0m2,947s user 0m2,886s sys 0m0,045s

## Slide 14: Lab
We will
Review PICINFO application
Review AVRInfo application
Edit Preferences application
Code portability

## Slide 16: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers, GC Code debugging
Summary

## Slide 17: GCBASIC
PIC16F175xx
Part 18 - The GCBASIC Tool Chain