## Slide 1: GCBASIC Part 15 - Interrupts
GCBASIC for the PIC18FxxQ20 chip Family
November 2024

## Slide 2: GCBASIC Part 15 - Interrupts
GCBASIC for the PIC18FxxQ20 chip Family
November 2024
Like and subscribe!

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the PIC – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 4: PIC18FxxQ20
PIC18-Q20 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI, I3C
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ20 offers 14 and 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 5: GCBASIC Toolchain
GCBASIC
Toolchain
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ20 chip family
GCBASIC simplifies the use of Interrupts

## Slide 6: Principles of Interrupts
Interrupts are events that alter the normal execution flow of a program to respond to external or internal events.
Advantages
  Immediate response to critical events
  Efficient use of the microcontroller's resources
Types of Interrupts
  External Interrupts: Triggered by events on external pins (RB0/INT0, RB1/INT1, etc.)
  Timer Interrupts: Triggered by timer overflows or matches
  Peripheral Interrupts: Triggered by events from peripherals (USART, ADC, etc.)
  Software Interrupts: Triggered by software instructions
Key Registers
  INTCON: Controls global interrupt enable and individual interrupt flags
  PIE1, PIE2: Peripheral Interrupt Enable registers
  PIR1, PIR2: Peripheral Interrupt Request (flag) registers
Interrupt Service Routine (ISR)
  Special function that executes when an interrupt occurs
  Must be as short and efficient as possible to avoid delaying other operations

## Slide 7: Interrupts…
For specific details of the interrupts see the microcontroller datasheet
The first parameter is the GCBASIC identifier used in user code to expose the specific interrupt
16bitUniversalTimerAInterrupt:TU16AIE,TU16AIF
16bitUniversalTimerBInterrupt:TU16BIE,TU16BIF
ADCReady:ADIE,ADIF
ADThreshold:ADTIE,ADTIF
ActiveClockTuning:ACTIE,ACTIF
CCP1:CCP1IE,CCP1IF
CCP2:CCP2IE,CCP2IF
CRCComplete:CRCIE,CRCIF
CWG1ShutDown:CWG1IE,CWG1IF
ClockSwitchComplete:CSWIE,CSWIF
DMA1AbortInterrupt:DMA1AIE,DMA1AIF
DMA1DestinationCountInterrupt:DMA1DCNTIE,DMA1DCNTIF
DMA1OverrunInterrupt:DMA1ORIE,DMA1ORIF
DMA1SourceCountInterrupt:DMA1SCNTIE,DMA1SCNTIF
DMA2AbortInterrupt:DMA2AIE,DMA2AIF
DMA2DestinationCountInterrupt:DMA2DCNTIE,DMA2DCNTIF
DMA2OverrunInterrupt:DMA2ORIE,DMA2ORIF
DMA2SourceCountInterrupt:DMA2SCNTIE,DMA2SCNTIF
DMA3AbortInterrupt:DMA3AIE,DMA3AIF
DMA3DestinationCountInterrupt:DMA3DCNTIE,DMA3DCNTIF
DMA3OverrunInterrupt:DMA3ORIE,DMA3ORIF
DMA3SourceCountInterrupt:DMA3SCNTIE,DMA3SCNTIF
DMA4AbortInterrupt:DMA4AIE,DMA4AIF
DMA4DestinationCountInterrupt:DMA4DCNTIE,DMA4DCNTIF
DMA4OverrunInterrupt:DMA4ORIE,DMA4ORIF
DMA4SourceCountInterrupt:DMA4SCNTIE,DMA4SCNTIF
ExtInt0:INT0IE,INT0IF
ExtInt1:INT1IE,INT1IF
ExtInt1:INT1IE,INT1IF
ExtInt2:INT2IE,INT2IF
I2C1ErrorInterrupt:I2C1EIE,I2C1EIF
I2C1Interrupt:I2C1IE,I2C1IF
I2C1ReceiveInterrupt:I2C1RXIE,I2C1RXIF
I2C1TransmitInterrupt:I2C1TXIE,I2C1TXIF
LogicCell1Event:CLC1IE,CLC1IF
LogicCell2Event:CLC2IE,CLC2IF
LogicCell3Event:CLC3IE,CLC3IF
LogicCell4Event:CLC4IE,CLC4IF
NVMComplete:NVMIE,NVMIF
OscillatorFail:OSFIE,OSFIF
PORTABChange:IOCIE,IOCIF
PWM1MatchEvent:PWM1IE,PWM1IF
PWM2MatchEvent:PWM2IE,PWM2IF
PWM2PeriodEvent:PWM2PIE,PWM2PIF
PWMPeriodEvent:PWM1PIE,PWM1PIF
PortChange:IOCIE,IOCIF
SPIInterrupt:SPI1IE,SPI1IF
SPIReceiveInterrupt:SPI1RXIE,SPI1RXIF
SPITransmitInterrupt:SPI1TXIE,SPI1TXIF
ScanComplete:SCANIE,SCANIF
SoftwareInterrupt:SWIE,SWIF
Timer0Overflow:TMR0IE,TMR0IF
Timer1Gate:TMR1GIE,TMR1GIF
Timer1Overflow:TMR1IE,TMR1IF
Timer2Match:TMR2IE,TMR2IF
Timer4Match:TMR4IE,TMR4IF
UART1FramingErrorInterrupt:U1EIE,U1EIF
UART1Interrupt:U1IE,U1IF
UART1ReceiveInterrupt:U1RXIE,U1RXIF
UART1TransmitInterrupt:U1TXIE,U1TXIF
UART2FramingErrorInterrupt:U2EIE,U2EIF
UART2Interrupt:U2IE,U2IF
UART2ReceiveInterrupt:U2RXIE,U2RXIF
UART2TransmitInterrupt:U2TXIE,U2TXIF
VoltageFail:HLVDIE,HLVDIF

## Slide 8: Interrupt on Change (IOC)
Detects changes in the state of selected pins
Key Points
  Configuration: Set IO port.pin as inputs and configure the correct register for edge detection (rising or falling edge).
Interrupt Service Routine (ISR)
  Handles the interrupt event
Global Interrupt Enable (GIE):
  Enables the microcontroller to respond to interrupts

## Slide 9: Interrupt - IOC

## Slide 10: Interrupt Code
……
//IO ports setup
/* Interrupt-on-change enabled on the IOCx pin for a negative-going edge. Associated Status bit
and interrupt flag will be set upon detecting an edge. */
IOCAN3 = 1
//Sets up GIE, create handler for interrupt
On Interrupt PORTChange Call InterruptHandler
Do lots of code
Loop
Sub InterruptHandler
Dim SWState as BIT
'Save the switch state
SWState = SWITCHIN
'Toggle the LED
LEDD7 = !LEDD7
'a little delay to see if the switch has changed state
Do while SWITCHIN = SWState
wait 10 us
Loop
'We must clear this specific bit flag in software, the main IOC is cleare by the GCBASIC interrupt handler
IOCAF3 = 0
End Sub

## Slide 11: Lab
Walk the examples
View the scope

## Slide 13: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the PIC – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 14: GCBASIC Part 15 - Interrupts
GCBASIC for the PIC18FxxQ20 chip Family
November 2024