## Slide 1: GCBASIC
PIC16F175xx
Part 16 - Progmem, SAF memory, EEPROM and DATA blocks

## Slide 2: GCBASIC
PIC16F175xx
Part 16 - Progmem, SAF memory, EEPROM and DATA blocks

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC16F175xx
PIC16175xx is a high performance PIC16
  Digital and analog peripherals for flexible embedded control
  10-bit ADC for accurate analog signal conversion
  Multiple communication interfaces including UART (serial), I²C, and SPI
  PWM modules with CCP and 16-bit resolution for precise timing and motor control
  Configurable Logic Cells (CLCs) for custom hardware-level logic without external components
  Integrated op amps for onboard analog signal conditioning and amplification
The PIC16175xx offers 14, 20, 28, 40 and 44-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR & LGT microcontrollers
GCBASIC now supports the 16F175xx chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 16F175xx attached
  You have the 4 LEDs operating
  You have a POT connected
  You have SWITCHes connected
  You have a USB/TTL converter

## Slide 8: Hardware
Prototype Board
Power 5v0
Programmer
Switch
LEDs & resistors
Hardware // -------------------PORTA----------------
// Bit#: -7---6---5---4---3---2---1---0---
// IO: ------------------SW----------ADC-
// ----------------------------------
// -------------------PORTB----------------
// Bit#: -7---6---5---4---3---2---1---0---
// IO: ---------------------------------
// ---------------------------------
// ------------------PORTC-----------------
// Bit#: -7---6---5---4---3---2---1---0---
// IO: ----TX1---------LED-LED-LED-LED--
// ---------------------------------
//
// ------------------PORTE-----------------
// Bit#: -7---6---5---4---3---2---1---0---
// IO: ----------------MCLR-------------
// -----------------SW--------------

## Slide 9: Storage Overview Types
 | Type | Characteristics
1 | Progmem | Program, and, Storage Area Flash (SAF) block
2 | Data RAM | Volatile
3 | Data EEPROM | Consider as a peripheral

## Slide 10: Progmem
or
Progmem usage
  Your program
  and/or
  Reference data
  Pictures
Uses PFM direct addressing
Program
Program Flash Memory
PIC16F175xx
Program
Program Flash Memory
PIC16F175xx

## Slide 11: Progmem
or
Progmem usage
  Your program
  and/or
  Reference data
  Pictures
Uses PFM direct addressing
Program
Reference Data
Program Flash Memory
PIC16F175xx
Program
Reference Data
Program Flash Memory
PIC16F175xx

## Slide 12: SAF
SAF usage
  Reference data
  Must not be overwritten by user program – you MUST adjust program to NOT use SAF block
Uses SAF offset addressing
or
Program
SAF Data
Program Flash Memory
PIC16F175xx
Program
SAF Data
Program Flash Memory
PIC16F175xx
SAF is designated for storing non-volatile data and can be protected to ensure data integrity and security.

## Slide 13: Progmem
or
Progmem usage
  Your program
  and/or
  Reference data
  Pictures
Uses PFM direct addressing
Program
Reference Data
Program Flash Memory
PIC16F175xx
Program
Reference Data
Program Flash Memory
PIC16F175xx

## Slide 14: EEDATA & DATA Blocks
 | Type | Characteristics
1 | EEDATA | An EEPROM block or blocks of data that is programmed into the EEPROM
2 | DATA | An DATA block or blocks of data that is programmed just above your program
Both areas can be easily used for reference data

## Slide 15: Lab
Walk the examples
  PROGMEM
  SAF
  EEPROM and DATA blocks

## Slide 17: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using I2C GCLD display solutions
Using a SPI GLCD display solutions
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 18: GCBASIC
PIC16F175xx
Part 16 - Progmem, SAF memory, EEPROM and DATA blocks