## Slide 1: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 16 - Progmem, EEPROM and DATA blocks

## Slide 2: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 16 - Progmem, EEPROM and DATA blocks
January 2025

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC16Fxxxx
PIC16Fxxxx is a high performance PIC16
  Digital and Analog peripherals
  8 –bit or 10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
The PIC16 offers 8, 14,18,20, 28, 40 and 48-pin packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, EEPROM and DATA blocks
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC supports the 16Fxxxx chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the PIC attached
  You have the 4 LEDs operating
  You have a POT connected
  You have switches connected
  You have USB/TTL serial converter
  You have LCD

## Slide 8: Hardware
The PICDEM 2 Plus Demonstration Board
18-, 28- and 40-pin DIP sockets (although three sockets are provided, only one device may be used at a time)
On-board, +5V regulator for direct input from 9V, 100 mA AC/DC wall adapter or 9V battery, or hooks for a +5V, 100 mA regulated DC supply
RS-232 socket and associated hardware for direct connection to an RS-232 interface
Programmer/debugger connectivity supporting MPLAB® ICD 3, MPLAB REAL ICE, PICkit 2 and PICkit 3
PICkit Serial Connector for analysis of serial communications peripherals such as SPI or I2C™
5 k pot for devices with analog inputs
Three push button switches for external stimulus and Reset
Power-on indicator LED
Four LEDs connected to PORTB
On-board external oscillators including: a) Unpopulated DIP socket for canned crystal oscillator (Y2) b) RC oscillator circuit (R4, C3) c) Unpopulated holes for crystal connection (Y1) d) 32.768 kHz crystal for Timer1 clock operation (Y3)
32K x 8 Serial EEPROM
LCD display
Piezo buzzer
Prototype area for user hardware
Expansion Header for PICtail™ daughter card connectivity or user access to
MCUs
Microchip TC74 thermal sensor

## Slide 9: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Switches
TTL/USB
Hardware
------------PORTA---------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ------------SW2-------------ADC--
IO: ---------------------------------
------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
IO: ---------------------------------
------------PORTC----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: -----TX--------------------------
IO: ---------------------------------
------------PORTD----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ---------------------------------
IO: ---------------------------------
------------PORTE----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------RST---------------
IO: ---------------------------------

## Slide 10: Storage Overview Types
 | Type | Characteristics
1 | Progmem | Program
2 | Data RAM | Volatile
3 | Data EEPROM | Consider as a peripheral

## Slide 11: Progmem
or
Progmem usage
  Your program
  and/or
  Reference data
  Pictures
Uses PFM direct addressing
Program
Program Flash Memory
( 1 to 16 KW )
PIC16Fxxxx
Program
Program Flash Memory
( 1 to 16 KW )
PIC16Fxxxx

## Slide 12: Progmem
or
Progmem usage
  Your program
  and/or
  Reference data
  Pictures
Uses PFM direct addressing
Program
Reference Data
Program Flash Memory
( 1 to 16 KW)
PIC16Fxxxx
Program
Reference Data
Program Flash Memory
( 1 to 16 KW)
PIC16Fxxxx

## Slide 13: EEDATA & DATA Blocks
 | Type | Characteristics
1 | EEDATA | An EEPROM block or blocks of data that is programmed into the EEPROM
2 | DATA | An DATA block or blocks of data that is programmed just above your program
Both areas can be easily used for reference data

## Slide 14: Lab
Walk the examples
  PROGMEM
  EEPROM and DATA blocks

## Slide 16: Videos...
Install the hardware and make the board work – make LEDs work
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, many ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, EEPROM and DATA blocks
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 17: GCBASIC
PIC16Fxxxx chip Family ( Legacy )
Part 16 - Progmem, EEPROM and DATA blocks