## Slide 1: GCBASIC
PIC16F175xx
Part 2 – sequence the LEDs

## Slide 2: GCBASIC
PIC16F175xx
Part 2 – sequence the LEDs

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC16F175xx
PIC16165xx is a high performance PIC16
  Digital and analog peripherals for flexible embedded control
  10-bit ADC for accurate analog signal conversion
  Multiple communication interfaces including UART (serial), I²C, and SPI
  PWM modules with CCP and 16-bit resolution for precise timing and motor control
  Configurable Logic Cells (CLCs) for custom hardware-level logic without external components
  Integrated op amps for onboard analog signal conditioning and amplification
The PIC16175xx offers 14, 20, 28, 40 and 44-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 16F175xx chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCSTUDIO software
  Installed your programmer software
  Test that you have the 16F175xx attached

## Slide 8: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Hardware
'' -------------------PORTA----------------
'' Bit#: -7---6---5---4---3---2---1---0---
'' IO: ---------------------------------
''-----------------------------------------
''
'' -------------------PORTB----------------
'' Bit#: -7---6---5---4---3---2---1---0---
'' IO: ---------------------------------
''-----------------------------------------
''
'' ------------------PORTC-----------------
'' Bit#: -7---6---5---4---3---2---1---0---
'' IO: ---------------LED--LED-LED-LED--
''-----------------------------------------
''

## Slide 10: Make four LEDs flash in a sequence
Initialise
Set 1st LED
Delay
Reset
LEDPORT = O ?
Rotate the LEDPORT
No
Yes

## Slide 11: Workshop
Rotate the LEDs with a delay
Uses
  The register PORTC LEDs via a constant
  Rotate command()
  Simple logic

## Slide 13: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 14: GCBASIC
PIC16F175xx
Part 2 – sequence the LEDs