## Slide 1: GCBASIC
18FXXQ24 CHIPFAMILY

## Slide 2: GCBASIC 18FxxQ24
November 2024 release
GCBASIC
New chip family – the ADC challenge

## Slide 3: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 4: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ24 chip family
GCBASIC is a cross platform with common code translation

## Slide 5: The core compiler
GCBASIC Compiler
Source Code
Preprocessor
Libraries
Code Translator
Assembler
Linker
High Level Language
Assembly Language
ASM file
Absolute Machine Code
HEX file
8 bit PIC, AVR, AVR-DX and LGT
Reports:
TXT and HTML
GCBASIC Compiler
Chip Specific DAT file
Chip Specific Constraints

## Slide 6: Hardware
GCBASIC prototype board
  8, 14, 18, 28 and 40 pin devices
  LEDs
  Switches
  POTs
  Connections
    USB, GLCD, LCD
    Sensors
PICKit2 using PICKitPlus
External power supply

## Slide 7: LAB
Try to get ADC to show result on LEDs

## Slide 8: Summary findings
DAT memory specification section ( ‘[FreeRAM]’ ) was incorrect - resolved
  [FreeRAM] RAM location – fixed within GETCHIPDATA.BAS
ADC initially shows no results
  Wrong connection on the test rig!
Issue Noted
  Compiler does not handle undefined port.bit appropriate portc.7

## Slide 9: GCBASIC 18FxxQ24
November 2024 release
GCBASIC
Like and subscribe!
New chip family – getting the basics operating