## Slide 1: GCBASIC
PIC18FxxQ24
Part 3 - read the ADC

## Slide 2: GCBASIC
PIC18FxxQ24
Part 3 - read the ADC

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC18FxxQ24
PIC18-Q24 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ24 offers 28, 40 and 48-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC and AVR microcontrollers
GCBASIC now supports the 18FxxQ24 chip family

## Slide 7: Analog-to-Digital
We configure the ADC, run a conversion, read the analog voltage controlled by the potentiometer on the board, and display the results on the LEDs.

## Slide 8: Analog-to-Digital

## Slide 9: Analog-to-Digital
GCBASIC completes the initialisation
Create a variable to store the ADC results
Read the ADC
  GCBASIC makes the process easy via the ReadADC()
  ReadADC returns a value of 0 to 255
Set the LEDs
Do it again….

## Slide 10: Analog-to-Digital

## Slide 11: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 18FxxQ24 attached
  You have the 4 LEDs operating
  You have a POT connected

## Slide 12: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------------------ADC--
----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
----------------------------------------
------------------PORTC-----------------
Bit#: -X---6---5---4---3---2---1---0---
IO: -^-------------------------------
-----VDDIO2-----------------------------
You must apply correct Voltage

## Slide 13: Workshop
Read the ADC to set the LEDs
Uses
  A Byte variable
  Simple logic

## Slide 15: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 16: GCBASIC
PIC18FxxQ24
Part 3 - read the ADC