## Slide 1: GCBASIC
PIC18FxxQ24
Part 4 – sequence the LEDs

## Slide 2: GCBASIC
PIC18FxxQ24
Part 4 – sequence the LEDs

## Slide 3: GCBASIC
Like and subscribe!

## Slide 4: PIC18FxxQ24
PIC18-Q24 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C and SPI
    PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ24 offers 28, 40 and 48-pin products in small footprint packages to support customers in a wide variety of applications.

## Slide 5: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 6: GCBASIC Compiler
GCBASIC Compiler
GCBASIC is an Open Source compiler for PIC and AVR microcontrollers
GCBASIC now supports the 18FxxQ24 chip family

## Slide 7: Prerequisites
Assumes you have
  Installed the GCBASIC software
  Installed your programmer software
  Test that you have the 18FxxQ24 attached
  You have the 4 LEDs operating
  You have a POT connected

## Slide 8: Digital input

## Slide 9: Hardware
Prototype Board
Power 5v0
Programmer
LEDs & resistors
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------------------ADC--
----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: ----------------LED-LED-LED-LED--
----------------------------------------
------------------PORTC-----------------
Bit#: -X---6---5---4---3---2---1---0---
IO: -^-------------------------------
-----VDDIO2-----------------------------
You must apply correct Voltage

## Slide 10: Time
The tutoral combines previous tutorials by using the Analog-to-Digital Converter (ADC) to control the speed of rotation.
  Where speed is a time delay
    us, 10us, ms, 10ms, s, m or h
    wait time unit
    wait 1 ms

## Slide 11: Analog-to-Digital
GCBASIC completes the initialisation
Create a variable to store the ADC results
Read the ADC
  GCBASIC makes the process easy via the ReadAD10()
  ReadAD10 returns a value of 0 to 1023
Wait for a time period based on returned ADC value
Set the LEDs
Do it again….

## Slide 12: Wait
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Time delays are sometimes key to the operation of a program
Read ADC 10 bit
( 0 – 1023 )

## Slide 13: Rotate with Carry
 | LEDD3 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 14: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 15: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 16: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 17: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 18: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 19: Rotate with Carry
 | LEDD4 = C.4 | LEDD2 | LEDD1 | LEDD0 | CARRY = SREG.0
Start | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0
Rotate(shift) | 0 | 0 | 1 | 0 | 0
Rotate(shift) | 0 | 0 | 0 | 1 | 0
Rotate(shift) | 0 | 0 | 0 | 0 | 1
Restart | 1 | 0 | 0 | 0 | 0
Rotate(shift) | 0 | 1 | 0 | 0 | 0

## Slide 20: Carry Test
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Did it overflow ?
If C = 1 then .. Or other test condition
Read ADC 10 bit
( 0 – 1023 )

## Slide 21: Scale
Scale()
Scale transforms an existing value to a new value within a specified scale
Initialise
Set 1st LED
Wait for a Delay
Set 1st LED
Did it overflow ?
Rotate the LEDs
No
Yes
Read ADC

## Slide 22: Workshop
Read the ADC to set the LEDs
Uses
  A Byte variable
  Simple logic

## Slide 24: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 7 ways, to dim the LEDS
Using an external interrupt to control an LED
Using storage within the chip – Progmem, SAF memory, EEPROM and DATA blocks
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 25: GCBASIC
PIC18FxxQ24
Part 4 – sequence the LEDs