## Slide 1: GCBASIC Part 11
GCBASIC for the PIC18FxxQ20 chip Family
October 2024
I2C discovery!

## Slide 2: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to sequence the LEDs
Using memory within the PIC – Progmem and SAF memory
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 3: PIC18FxxQ20
PIC18-Q20 is a high performance PIC18
  Digital and Analog peripherals
  10-bit ADC
  Multiple communication interfaces
    Serial, I2C, SPI, I3C
  PWM – CCP/PWM and 16Bit
  Configurable Logic Cells
  Multi voltage domains
The PIC18xxQ20 offers 14 and 20 pin products in small footprint packages to support customers in a variety of space constrained and sensor node applications.

## Slide 4: GCBASIC Toolchain
GCBASIC
Toolchain
GCBASIC is an Open Source compiler for PIC, AVR and LGT microcontrollers
GCBASIC now supports the 18FxxQ20 chip family
GCBASIC simplifies the use of I2C

## Slide 5: I2C
I2C uses two bidirectional open collector or open drain lines pulled up with resistors
  Serial Data Line (SDA)
  Serial Clock Line (SCL)
Typical voltages used are +5 V or +3.3 V, although systems with other voltages are permitted

## Slide 6: Hardware
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: -----------------SW---------ADC--
-----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: TX--SCK-SDA--^-------------------
------------------VDDIO3---------------- You must apply correct Voltage
------------------PORTC-----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: LED-LED-LED-LED------^-----------
--------------------------VDDIO2-------- You must apply correct Voltage
Prototype Board
Power 5v0
Programmer
Serial Port
LEDs & resistors
Potentiometer
Switch

## Slide 7: Hardware
Hardware
-------------------PORTA----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: -----------------SW---------ADC--
-----------------------------------------
-------------------PORTB----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: TX--SCK-SDA--^-------------------
------------------VDDIO3---------------- You must apply correct Voltage
------------------PORTC-----------------
Bit#: -7---6---5---4---3---2---1---0---
IO: LED-LED-LED-LED------^-----------
--------------------------VDDIO2-------- You must apply correct Voltage
Prototype Board
Power 5v0
Programmer
Serial Port
LEDs & resistors
Potentiometer
Switch

## Slide 8: Setup
CLOCK
DATA
VCC

## Slide 9: I2C

## Slide 10: Lab
Examine the sample code
  Using PPS select the I2C ports
  Using PPS select the serial USART port
  Set up the I2C
  Review the code
  See the results

## Slide 12: Videos...
Install the hardware and make the board work – three LED programs
Make four LEDs flash in a sequence
Set the LEDs to represent the value of ADC
Sequence the LEDs with a delay using the value of ADC
Using an input to set the state of the LEDs
Using the reset switch
Using the switch, ADC – make the LEDs flash in a sequence with reverse
Using the serial to display values
Using the timer0 overflow, 8bit timer, 16bit timer to flash the LEDs
Using EEProm – showing values on the serial terminal, and more constants insights
Using I2C with serial to discover I2C devices
Using an I2C GCLD display
Using a SPI GCLD display
Using PWM, 6 ways, to dim the LEDS
Using an external interrupt to sequence the LEDs
Using memory within the PIC – Progmem and SAF memory
Using CLC
The GCBASIC tool chain
Assembly , alternatives assemblers and MPLAB-X
Summary

## Slide 13: GCBASIC Part 10
GCBASIC for the PIC18FxxQ20 chip Family
October 2024

## Slide 15: Backup Slides

## Slide 16: I2C